## Slide 1: Smart Ring Spinning Optimization in Textile Industry
Department of Electrical Engineering,
University of Engineering and Technology, Lahore
Group No: 41
Project Advisor: Dr. Ubaid Ullah Fayyaz
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 2: Team Introduction
Saqib Nisar
2017-EE-045
Specialization: Computing
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021
Muhammad Usman Khan
2017-EE-187
Specialization: Computing
Muhammad Suleman
2017-EE-166
Specialization: Computing
Usama Amir
2017-EE-043
Specialization: Power

## Slide 3: Problem Statement
The main problem concern in textile Industry is a thread break while bobbin build up.
End break detection is only possible if a staff member detects that end breaks as soon as possible.
Also due to end break, there is no control over the yarn delivery rollers unless the staff member figure that out.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 4: Proposed Solution
The product that we will make will measure and control the critical parameters in ring spinning.
End-break detection with our product is the starting point for best-practice in optimization.
After break detection, the data of bobbin is analyzed through programming and emergency light will glow that will show that the thread is broken.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 5: Block Diagram
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 6: Flow Diagram
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 7: Applications
Increase Yield of industry
Workload on staff members decrease
No need of periodical maintenance
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 8: Audience
Target Audience will be all textile industries of Pakistan.
Complete Working prototype will be made at the end and its working will be demonstrated in the industries.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 9: Simulation
Stages
Three major stages of circuit for thread break detection:
      Stage 1 (Signal Conditioning Circuit)
      Stage 2 (Inverting Amplifier Circuit)
      Stage 3 (Schmitt Trigger Circuit)
  Stage 1 (Signal Conditioning Circuit)
      Common Emitter Component
      Comparator Component
      Low Pass Filter Component
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 10: Simulation
  Stage 2 (Inverting Amplifier Circuit)
      Amplify the detecting signal
      Standard gain achieved
      Low Pass Filter
  Stage 3 (Schmitt Trigger Circuit)
      Upper and Lower Threshold
      Remove Any type of noise
      Square wave obtain of varying frequency
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 11: Simulation & Calculation
  Schmitt Trigger Calculations and Complete Circuit
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 12: Hardware Developed
Motor Design:
      A2212/ T10 1400kV BLDC Motor
      Max. Efficiency Current: 6-12A
      Max. Watts: 180W
      Max Efficiency: 80%
Prototype Setup:
      12V power supply
      BLDC
      ESC
      Arduino
      potentiometer
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 13: Hardware Developed
Arduino Code for the Motor Setup:
      The following code configures the motor setup including power supply, BLDC, ESC, Arduino and potentiometer.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 14: Hardware Developed
Arduino Code for RPM calculation:
  The following code
  determines the rpm
  and frequency of the
  prototype e.g.
  motor setup->IR sensor
  ->signal conditioning->
  amplifier-> comparator
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 15: Hardware Developed
Prototype Final Testing:
    The final step in hardware was final testing of the prototype. The circuit was patched, motor was started and the Arduino codes helped us find the frequency and rpm of the spinning prototype.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 16: Software Developed
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021
Master/Slave Nomenclature
In our project, the rpm of each spindle is recorded by micro-controller called Slave.
Four spindles are connected to one slave and 24 slaves are connected to one micro-controller called Master.
This whole network of Master/Slave is connected in Modbus configuration and RS-485 protocol is followed for the communication.
Four master controllers are joined with one R-pi to gather all the data and upload it to cloud.
The Master acts according to slave data and notify the operator about the fault
Figure: Modbus

## Slide 17
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021
Serial Communication
The communication between master and slaves is serial with baud rate of 9600
Master sends request to each slave which comprises of the slave id and function code
Upon matching with the id, the directed slave sends it data, rpm and timestamp, in byte array/data frame
The data frame/byte array varies according to the function code in master’s request i.e. what data is requested from the salve
Master repeats this process after every 0.5s

## Slide 18: Master – R-Pi Communication
R-Pi is used to transferred data to Cloud
4 Masters are connected to 1 R-Pi
Protocol used for Communication is RS485
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 19
R-Pi to Cloud
MQTT is used to transfer
data from R-Pi to Cloud
It is lossless, bi-directional
and ordered protocol
It takes data from R-Pi
and deliver it to a single place
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 20: Future Deliverables
Adding more functional code to slave’s code e.g. to set the initial id’s at reset, acquiring duration of yarn breakage from slave etc..
Allotting separate ids to spindles in order to correctly identify the fault
Customizing Arduino-mini to be used with limited area and ports in our project
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 21: Gantt Chart
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021

## Slide 22: References
M Hossain, A Abdkader, A Nocke, R Unger, F Krzywinski, MMB Hasan, and Chokri Cherif. Measurement methods of dynamic yarn tension in a ring spinning process. Fibres & Textiles in Eastern Europe, 2016.
RZtronics and Instructables. Control brushless motor using arduino, Sep 2017. URL https://www.instructables.com/ Control-Brushless-Motor-Using-Arduino/.
Lammert Bies © 1997-2019. Rs485, specifications and in depth tutorial. URL https://www.lammertbies.nl/comm/info/rs-48
Qingguang Chen, Lingyun Xue, and Huanle Rao. Rotational speed measurement of ring spinning based on magnetic sensor. Measurement Science and Technology, 28(11):115106, 2017.
Undergraduate Final Year Project Presentation
Dated: 20th October, 2021